## Slide 1: An overview the ASTRID2 storage ring and its RF system
Jørgen S. Nielsen
Institute for Storage Ring Facilities (ISA)
Aarhus University
Denmark

## Slide 2: ASTRID2
ASTRID2 is the new synchrotron light source to be built in Århus, Denmark
Dec 2008: Awarded 5.0 M€ for
  Construction of the synchrotron
  Transfer of beamlines from ASTRID1 to ASTRID2
  New multipole wiggler
  We did apply for 5.5 M€
    Cut away an undulator for a new beamline
      Has to be financed together with a new beamline
    Saved some money by changing the multipole wiggler to better match our need

## Slide 3: ASTRID2 main parameters
  Electron energy: 580 MeV
  Emittance: 12 nm
  Beam Current: 200 mA
  Circumference: 45.7 m
  6-fold symmetry
    lattice: DBA with 12 combined function dipole magnets
      Integrated quadrupole gradient
  4 straight sections for insertion devices
  Will use ASTRID as booster (full energy injection)
    Allows top-up operation

## Slide 4: ASTRID2 Layout

## Slide 5: ASTRID2 Layout

## Slide 6: ASTRID2 details
General parameters |  | ASTRID2 | ASTRID
Energy | E [GeV] | 0.58 | 0.58
Dipole field | B [T] | 1.192 | 1.6
Circumference | L [m] | 45.704 | 40.00
Current | I [mA] | 200 | 200
Revolution time | T [ns] | 152.45 | 133.43
Length straight sections | [m] | ~3 | 
Number of insertion devices |  | 4 | 1
Lattice parameters |  |  | 
Straight section dispersion | [m] | 0 | 2.7
Horizontal tune | Qx | 5.23 | 2.29
Vertical tune | Qy | 2.14 | 2.69
Horizontal chromaticity | dQx/d(Δp/p) | -6.4 | -4.0
Vertical chromaticity | dQy/d(Δp/p) | -11.2 | -7.1
Momentum compaction | αp | 0.0107 | 0.068
Coupling factor |  | 5 % | 5 %
Synchrotron Radiation parameters |  |  | 
Synchrotron radiation integrals | I1 [m] | 0.488182 | 2.7164
 | I2 [m-1] | 3.870433 | 5.2016
 | I3 [m-2] | 2.384181 | 4.3060
 | I4 [m-2] | -1.457685 | 1.8615
 | I5 [m-1] | 0.130774 | 0.9363
Energy loss per turn | U0 [keV/turn] | 6.2 | 8.3
Synchrotron radiation power | P0 [kW] | 1.2 | 1.6
Natural emittance | εH [nm] | 12.1 | 140
Diffraction limit | λ [nm] | 38-101 | 1759
Characteristic wavelength | λc [nm] | 4.6 | 3.5
Characteristic energy | εc [eV] | 267 | 358
Horizontal damping time | τh [ms] | 20.7 | 29.1
Vertical damping time | τv [ms] | 28.6 | 18.7
Longitudinal damping time | τs [ms] | 17.6 | 7.9
RF parameters |  |  | 
Damped energy spread | σE/E [0/00] | 0.433 | 0.416
Damped bunch length | [cm] | 2.2 | 6.5
RF frequency | [MHz] | 104.950 | 104.950
Revolution frequency | [MHz] | 6.56 | 7.5
Harmonic number | h | 16 | 14
RF voltage | [kV] | 50 | 30
Overvoltage factor | q | 8.1 | 4
Quantum lifetime |  | ∞ | ∞
Synchrotron frequency | υ=Ω/2π [kHz] | 10 | 20.6

## Slide 7: ASTRID2 lattice

## Slide 8: ASTRID2 Status
Sep. 2009: Order of
  Magnets on girders for the synchrotron
    Dipoles, Q-poles, Sextupoles, correctors
  Fast magnets with power supplies
    Extr. Kicker, fast bumpers, inj. Septum
Timeline
  -2010: Design and order remaining items
  2011: Build and commission synchrotron
  2012: First beamlines on ASTRID2
  2013: All beamlines transferred to ASTRID2

## Slide 9: ASTRID2 RF
105 MHz (like ASTRID)
Main RF parameters
  Harmonic: 16
  RF voltage: 50-150 kV
  Synchrotron frequency: 10-17 kHz
  Synchrotron radiation power: ~1.4 kW
  Cavity power: 0.8-7 kW
10 kW tube-based FM transmitter (triode)
  Tube-based FM transmitters are
    Cheaper
    More robust

## Slide 10: ASTRID2 Cavity
Collaboration with MAX-lab
  MAX-lab needs 8 cavities (100 MHz) for MAX IV
    We need 2 cavities (105 MHz) (a spare for ASTRID1)
  New MAX-lab cavity
    Based on MAX II cavity
    Use Electron Beam Welding instead of vacuum brazing
    Proposal: Have industry build after MAX-lab RF design
  MAX-lab will also build a 300 MHz Landau cavity

## Slide 11: New ASTRIDx LLRF
We will need a new LLRF for ASTRID2
The present ASTRID LLRF is
  Old, Analog
    Risk of failure, not easy to repair/maintain
We are seeking a solution which is
  Simple (we have limited resources)
  Adequate
Two possibilities
  Fully digital:
    Direct digital sampling of down converted signals
      Others achieve 0.1% stability
  Analog down conversion to baseband
    Digital control of baseband signals
      Stability: ~1%

## Slide 12: ASTRIDx LLRF (proposal)
Digital control of baseband signal
  Either with IQ modulators and demodulators or with amplitude and phase
  A computer (PC) running LabVIEW Real-Time with FPGA equipped multifunction card to measure and control the baseband signals
    NI PCIe-7851R/7852R:
      Virtex 5 FPGA, 8 AI, 750 kS/s/ch, 8 AO, 1 MS/s/ch, 16 bit
      PID Loop rates in excess of 100 kHz
        Cavity fill time has a 3 dB point at 6 kHz
We believe this solution is
  Simple, but adequate
  Flexible
  Allows easily integrated diagnostics

## Slide 13: ASTRIDx LLRF proposal
PreAmp
+40 dB, 10 W
FM transmitter
+36 dB, 10 kW
Splitter
Master oscillator 104.95 MHz
Rohde&Schwarz SMY01 or DDS
Combiner
Phase
shifter
Atten-
nuator
-5 –
-55 dB
-180° –
+180°
optional
Fast feedback loop
Dx
RF splitter
DM1
DM2
Dx
Realtime computer with IO (e.g. PC (or an NI Compact RIO) with LabVIEW RealTime)
adcMOlevel
dacA
dacφ
MO
MO
adcCavQ
adcCavI
adcFPWQ
adcFPWI
dacPlunger
adcRPW
Attenuator/
gain
-33 –
+25 dB
Phase
shifter
-180° –
+180°

## Slide 14: Conclusions
Have shown you
  The new ASTRID2 SR source
  The RF system for ASTRID2
  Proposal for new ASTRIDx LLRF
Would appreciate feedback on our ideas
  Analog system (digital control of baseband signals)?
  Fully digital system with fast sampling of down converted signal?
    Do we need the higher stability?